## Slide 1
John Wamburu, Christopher Raff, David Irwin and Prashant Shenoy
University of Massachusetts, Amherst
Greening Electric Bike Sharing Using Solar Charging Stations

## Slide 2: Rise of ride sharing
Catapulted by the ubiquity of smartphones
Mostly made up of car-based sharing and bike sharing
High carbon emissions

## Slide 3: Research question
How can we make ride sharing greener?
Focus on electric bike sharing
  How can we make an electric bike sharing system zero carbon?

## Slide 4: Electric bikes (E-bikes)
Type of small EV
Powered by electric grid
Requires electric charging infrastructure
Not zero-carbon
How can we make electric bike sharing zero carbon?

## Slide 5: Outline
Introduction
Hardware design of a solar charging station
Analysis of an electric bike sharing system
Conclusions

## Slide 6: Prototype solar charging station design
Design Goals
Harvest enough solar energy to charge bikes docked at a station
Enough solar array to charge during the day
Have enough storage for backup energy during low solar hours e.g. night

## Slide 7: Prototype data analysis
Able to generate 0.54kWh per day on single panel
Enough to charge 2 bikes to full capacity
Able to charge single bike battery from zero to full capacity in 3 hours

## Slide 8: Designing an electric bike sharing system
How many solar panels and battery capacity are required in an entire bike sharing system?
  Grid-tied design
  Off-grid design

## Slide 9: Analysis of an electric bike sharing system
59 Stations
490 Bikes
70,076 Trips
1 Year

## Slide 10: Grid-tied net zero carbon design
Key result: A single panel installed at each station is capable of meeting entire annual energy demand.
Max annual energy consumption: 267kWh
Single 320W panel generation: 296kWh

## Slide 11: Off-grid true zero carbon design
Key result: an off-grid design requires approximately 2 panels per station in the average case, which is 2x higher than a net-metered design
No. of panels required by season
Max no. of panels across seasons

## Slide 12: Battery size and panel tradeoff
Key result: there exists a tradeoff between the size of solar array installed and the required battery size per station
Battery size per station
Battery size and panel array tradeoff

## Slide 13: Carbon benefits
Key results
Carbon emission reduction is realized in both off-grid and grid-tied designs
Emission reduction in net-metered design much higher due to added benefit of injecting excess solar generation into the grid
Total emission reduction in off-grid design: 0.2MT
Total emission reduction in net-metered design: 1.1MT

## Slide 14: Conclusions
We presented the design of a solar powered bike charging station
We showed the feasibility of the design in off-grid and net-metered designs
We showed that a single panel is sufficient to meet the annual energy demand of a station in the net-metered design
In the off-grid design, this is approximately 2x panels
Finally, we showed that up to 1.1MT of CO2 emission can be reduced annually by substituting grid energy with solar

## Slide 15: Acknowledgements
Lab. for Advanced Software Systems: http://lass.cs.umass.edu
ValleyBike bike share system: https://www.valleybike.org/
NSF grant 1645952 and MA Department of Energy Resources.

## Slide 16: Thanks!
John Wamburu jwamburu@cs.umass.edu University of Massachusetts Amherst