## Slide 1
Noman Bashir, Prashant Shenoy, and David Irwin
University of Massachusetts, Amherst
DeepSnow: Modeling the Impact of Snow on
Solar Generation

## Slide 2: Solar is the future
Solar power is rapidly increasing
  Up to 100MW solar PV added world-wide each day1
  On track to be the largest source of electricity by 2050
Other forms of energy cannot compete with solar
  Cost decreasing at scale and with increase in efficiency
  Low maintenance, fuel-less operation, and ease of installation
1 source: www.iea.org, figure source: renewable global status report

## Slide 3: Solar power is highly variable
High sensitivity to environmental conditions
  Primarily affected by clouds, temperature, and snow.
How to mitigate the variability challenge?
  Use storage to smooth out fluctuations
    Still expensive, progress lags solar
  Accurately model and predict solar output
    Help plan energy supply, value solar sites for financing
Sunny - cold
Cloudy
Sunny - hot
Snow

## Slide 4: Solar performance modeling is an active research area
Models estimate site’s current or future output
  Based on site’s characteristics, i.e. tilt, and environment, i.e. cloud
  Many models available, i.e. pvlib, SAM, Solar-TK
Models above are generally highly accurate
  Work well under clear sky; decent under clouds
  Accuracy degrades significantly under snow
System
Advisor
Model
(SAM)
Solar-TK

## Slide 5: Modeling effect of snow is important
Some regions with high solar growth are snowy
  Examples are Massachusetts and Germany
Variability in solar is disproportionately affected by snow
  Short-term uncertainty complicates grid operation
  Long-term inaccuracy impacts return-on-investment
Chart: Energy (kWh)
| March'18 | March'19
Series 1 | 256 | 774
Chart: Percentage (%)
| Jan-March | Other months
Contribution to energy | 8 | 92
Contribution to variability | 65 | 35
8
Variability is due to snow
Solar varies over years

## Slide 6: A simple model is not enough
Snow effect is more complex than just snow depth
Simple model:
if snow depth > x
output = 0
  Prior work suggests
  x to be 1-5cm

## Slide 7: Factors affecting solar power under snow
Optical properties of snow determine power output
  Snow depth is one of the factors affecting opaqueness
  Dependent on flake size, density, water content, etc.
Public snow data is not same as snow on panel surface
  Weather stations generally dozens of miles away
  Data measured on flat ground, wood board, or grass
  Solar panels are tilted and possibly under shadows

## Slide 8: Rest of the talk
Snow data analysis
DeepSnow modeling approach
Implementation and evaluation

## Slide 9: Snow effect is complex
Snow data from NOHSRC1
  40+ snow related variables; modeled or observed
  Data cleaning: reporting %age and correlation
Factors too numerous and complex to physically model
  Effect of individual variables can possibly be modeled
  No physical model exists combining all variables
1National Operational Hydrologic Remote Sensing Center
Snow depth (modeled) | Snow depth (observed) | Snow precipitation | Non-snow precipitation
Dew-point temperature | Air temperature | Wind speed | Humidity

## Slide 10: Snow data on panel surface is more complex
Site characteristics impact actual snow on panel
  Sliding because of panel tilt and low surface friction
  Low melting rate under shadow from nearby objects

## Slide 11: High tilt leads to more snow slide
higher tilt  high power output
*Sites ordered by increasing tilt ranging from 15° to 60°

## Slide 12: Shading prevents snow from melting
Shaded sites generate less energy
*Sites in each group are within 1 mile of each other on a snowy day

## Slide 13: Snow complexity suits deep learning
Solar performance model output w/o snow effect
DeepSnow Model snow adjustment factor
Range: 0 -1
snow-adjusted
generation
DeepSnow
Model Trainer
DeepSnow
parameters
Snow data
Tilt, orientation
Snow loss factor
(SAM)
Shading factor
(Solar-TK)
optional features
required
output
Framing deep learning approach is non-trivial
  Decouple the effect of snow from other variables, i.e. cloud
  Leverage existing work on solar performance modeling

## Slide 14: Evaluation setup
Dataset: hourly data for actual solar sites
  10 solar sites across CO, IL, MA, MN, and NY
  Site capacities in 1kW to 50kW range
Evaluation Metric: Short- and long-term accuracy
  Short- and long-term: instant. power and annual energy
  Mean Absolute Percentage Error (MAPE)
    Lower MAPE means high accuracy
Baseline: Solar-TK and SAM
  No snow model in Solar-TK
  SAM models slide based on temp. and tilt

## Slide 15: Evaluation: annual energy estimate
DeepSnow performs outperforms SAM for all sites
~9% reduction
in MAPE
~50% reduction
in MAPE

## Slide 16: Evaluation: power output estimate
DeepSnow outperforms SAM for all sites

## Slide 17: Evaluation: power output estimate in winter
Winter improvement is much more significant
~54% reduction
in MAPE
~95% reduction
in MAPE

## Slide 18: Conclusion
Modeling effect of snow on solar is important
Snow effect is complex and cannot be physically modeled
DeepSnow leverages deep learning
  Using publicly available snow data
  Leverages prior work on solar modeling
DeepSnow outperforms state-of-the-art models

## Slide 19: Open to questions
Contributions
  Modeling the effect of snow on solar output is important
  At places with snow, it is the major cause of variability
  Modeling the effect of snow is challenging
  We improve state of the art